## Slide 1: MGT 214 OPERATIONS MANAGEMENT
CHAPTER 06
Layout Decisions
Prepared by: Ms. Dalal Bamufleh

## Slide 2: MCDONALD’S LOOK FOR COMPETITIVE ADVANTAGE THROUGH LAYOUT

## Slide 3: MCDONALD’S LOOK FOR COMPETITIVE ADVANTAGE THROUGH LAYOUT
Indoor seating (1950s)
Drive-through window (1970s)
Adding breakfast to the menu (1980s)
Adding play areas (late 1980s)
Redesign of the kitchens (1990s)
Self-service kiosk (2004)
21st Century look: 3 dining sections

## Slide 4: MCDONALD’S LOOK FOR COMPETITIVE ADVANTAGE THROUGH LAYOUT
Three separate dining areas
  Linger zone with comfortable chairs and Wi-Fi connections
  Grab and go zone with tall counters and with bar stools.
  Flexible zone for kids and families with colorful and movable furniture
Facility layout is a source of competitive advantage (CSF)

## Slide 5: Strategic Importance of Layout Decisions
The objective of layout strategy is to develop an effective and efficient layout that will meet the firm’s competitive needs and requirements.
An effective layout can help an organization achieve a strategy that support differentiation, low cost or response.

## Slide 6: Strategic Importance of Layout Decisions
Layout Design Considerations:
  Higher utilization of space, equipment, and people
  Improved flow of information, materials, or people
  Improved employee morale and safer working conditions
  Improved customer/client interaction
  Flexibility
Layout designs needs to be viewed as dynamic

## Slide 7: Types of Layout
Office layout
Retail layout
Warehouse layout
Fixed-position layout
Process-oriented layout
Work-cell layout
Product-oriented layout

## Slide 8: Types of Layout
Good layouts requires determining the following:
  Material handling equipment
  Capacity and space requirements
  Environment and aesthetics
  Flows of information
  Cost of moving between various work areas

## Slide 9: Office Layout
Requires the grouping of workers, their equipment, and spaces to provide comfort, safety, and movement of information
Movement of information is main distinction
Typically in state of flux due to frequent technological changes
Electronic data and paper work
Relationship chart

## Slide 10: Office Layout
Some of the universal layout considerations: working conditions, teamwork, authority …etc
Private or open cubicles?
Open Cubicles
Private Cubicles

## Slide 11: Office Layout
Private office
Low or high file cabinets

## Slide 12: Office Layout
Same entrance, rest room, lockers and cafeteria for all employees?
Two major trends:
  Technology such as cell phone, iPods, faxes, Internet, and laptop computers increase layout flexibility.
  Modern firms create dynamic needs for space and services.

## Slide 13: Retail Layout
Objective is to maximize profitability per square foot of floor space
Sales and profitability vary directly with customer exposure
OM try to expose customers to as many products as possible
 rate of exposure,  sales and  return on investment
How to change exposure?

## Slide 14: Retail Layout
Five Helpful Ideas for Supermarket Layout:
Locate high-draw items around the periphery of the store
Use prominent locations for high-impulse and high-margin items
Distribute power items to both sides of an aisle and disperse them to increase viewing of other items
Use end-aisle locations
Convey mission of store through careful positioning of lead-off department

## Slide 15: Retail Layout
Category Management
Slotting fees: Manufacturers pay fees to retailers to get the retailers to display (slot) their product
Contributing factors:
  Limited shelf space
  Massive new products
  Limit small firms ability to expand

## Slide 16: Retail Layout
Servicescapes:
  Ambient conditions - background characteristics such as lighting, sound, smell, and temperature
  Spatial layout and functionality - which involve, aisle characteristics (width, direction, shelf spacing...etc.) , and product grouping
  Signs, symbols, and artifacts - characteristics of building design that carry social significance e.g.: Wal-Mart greeter at the door, Disneyland's entrance

## Slide 18: Warehousing and Storage Layouts
Objective is to optimize trade-offs between handling costs and costs associated with warehouse space
Maximize the utilization of the total “cube” of the warehouse – utilize its full volume while maintaining low material handling costs

## Slide 19: Warehousing and Storage Layouts
Material Handling Costs:
All costs associated with the transaction
    Incoming transport
    Storage
    Finding and moving material
    Outgoing transport of the materials to be warehoused
    Equipment, people, material, supervision, insurance, and depreciation
Minimize damage and spoilage

## Slide 20: Warehousing and Storage Layouts
Automated Storage and Retrieval Systems (ASRSs) can significantly improve warehouse productivity

## Slide 21: Warehousing and Storage Layouts
An important component of warehouse layout is the relationship between the receiving/ unloading area and the shipping/ loading area.

## Slide 22: Warehousing and Storage Layouts
1. Cross-Docking
Materials are moved directly from receiving to shipping and are not placed in storage in the warehouse
Reduces distribution, inventory and facility costs
Requires tight scheduling and accurate product identification e.g. bar code

## Slide 23: Warehousing and Storage Layouts
2. Random Stocking
Typically requires automatic identification systems (AISs) and effective information systems
Random assignment of stocking locations allows more efficient use of space
Key tasks:
  Maintain list of open locations
  Maintain accurate records of existing inventory and its locations
  Sequence items to minimize travel, and pick time
  Combine picking orders to reduce picking time
  Assign classes of items to particular areas
 facility utilization,  labor cost, but requires very accurate records

## Slide 24: Warehousing and Storage Layouts
3. Customizing
Value-added activities performed at the warehouse
  Assembly of components
  Loading software
  Repairs
  Customized labeling and packaging

## Slide 25: Fixed-Position Layout
Project remains in one place and workers and equipment come to site
E.g.: ship, highway, bridge, house, operation room
Complicating factors
  Limited space at site
  Different materials required at different stages of the project
  Volume of materials needed is dynamic

## Slide 26: Fixed-Position Layout
Alternative Strategy
  As much of the project as possible is completed off-site in a product-oriented facility
  This can significantly improve efficiency but is only possible when multiple similar units need to be created

## Slide 27: Work Cells
Reorganizes people and machines into groups to focus on single products or product groups
Volume must justify cells
Group technology identifies products that have similar characteristics for particular cells
Cells can be reconfigured as designs or volume changes

## Slide 28: Work Cells
Improving Layouts Using Work Cells
Current layout - workers in small closed areas. Cannot increase output without a third worker and third set of equipment.
Improved layout - cross-trained workers can assist each other. May be able to add a third worker as additional output is needed.
U-shaped line may reduce employee movement and space requirements while enhancing communication, reducing the number of workers, and facilitating inspection
+

## Slide 29: Work Cells
Improving Layouts Using Work Cells
Current layout - straight lines make it hard to balance tasks because work may not be divided evenly
Improved layout - in U shape, workers have better access. Four cross-trained workers were reduced.
U-shaped line may reduce employee movement and space requirements while enhancing communication, reducing the number of workers, and facilitating inspection

## Slide 30: Process-Oriented Layout
Low volume,  high variety
Like machines and equipment are grouped together
Efficient when making products with different requirements, or when handling different needs of customers
Each product requires different sequence of operations
E.g.: ER Process

## Slide 31: Process-Oriented Layout
Surgery
Radiology
ER triage room
ER Beds
Pharmacy
Emergency room admissions
Billing/exit
Laboratories
Patient A - broken leg
Patient B - erratic heart pacemaker

## Slide 32: Process-Oriented Layout
Advantages:
  Flexibility
  Capability of handling a wide variety of products or services
Disadvantages:
  General-purpose use of equipment  labor skills and cost,  required level of training and experience
  Orders take more time to move through the system because of difficult scheduling, changing setup, and unique material handling

## Slide 33: Process-Oriented Layout
Arrange departments/ work centers so as to minimize the costs of material handling
Material handling cost in this approach depend on:
  Number of loads (or people) moving between centers
  Distance-related cost of moving loads (or people) between centers

## Slide 34: Process-Oriented Layout
Designing process- oriented layout steps:
  Construct a “from-to matrix”
  Determine the space requirements
  Develop an initial schematic diagram
  Determine the cost of this layout
  Try to improve the layout
  Prepare a detailed plan

## Slide 35: Process-Oriented Layout
Department Assembly Painting Machine Receiving Shipping Testing
(1) (2) Shop (3) (4) (5) (6)
Assembly (1)
Painting (2)
Machine Shop (3)
Receiving (4)
Shipping (5)
Testing (6)
Department Assembly Painting Machine Receiving Shipping Testing
(1) (2) Shop (3) (4) (5) (6)
Assembly (1) 50 100 0 0 20
Painting (2) 30 50 10 0
Machine Shop (3) 20 0 100
Receiving (4) 50 0
Shipping (5) 0
Testing (6)
Number of loads per week
Example 1:
Page: 385
  1. Construct a “from-to matrix”

## Slide 36: Process-Oriented Layout
  2. Determine the space requirements
Area 1 Area 2 Area 3
Area 4 Area 5 Area 6
60’
40’
Receiving Shipping Testing
Department Department Department
(4) (5) (6)
Assembly Painting Machine Shop
Department Department Department
(1) (2) (3)

## Slide 37: Process-Oriented Layout
  3. Develop an initial schematic diagram
100
50
20
50
50
20
10
100
30
Machine Shop (3)
Testing
(6)
Shipping
(5)
Receiving
(4)
Assembly
(1)
Painting
(2)

## Slide 38: Process-Oriented Layout
  4. Determine the cost of this layout
X= Number of loads
C= Cost for moving load
The cost of moving adjacent department is estimated to be $1, and 2$ for nonadjacent departments.
Cost = ∑ ∑ Xij Cij
n
i = 1
n
j = 1
Cost = $50 + $200 + $40
(1 and 2) (1 and 3) (1 and 6)
+ $30 + $50 + $10
(2 and 3) (2 and 4) (2 and 5)
+ $40 + $100 + $50
(3 and 4) (3 and 6) (4 and 5)
= $570

## Slide 39: Process-Oriented Layout
  5. Try to improve the layout
30
50
20
50
10
20
50
100
100
Machine Shop (3)
Testing
(6)
Shipping
(5)
Receiving
(4)
Painting
(2)
Assembly
(1)
Cost = 50 + (30X2) + 10 + 50 + 100 + 20 + 100 + (20X2) +50
= $ 480

## Slide 40: Process-Oriented Layout
  6. Prepare a detailed plan
Area 1 Area 2 Area 3
Area 4 Area 5 Area 6
60’
40’
Receiving Shipping Testing
Department Department Department
(4) (5) (6)
Painting Assembly Machine Shop
Department Department Department
(1) (2) (3)

## Slide 41: Repetitive and Product-Oriented Layout
 High volume,  low variety products
Repetitive production and continuous production use product layout.
Two types of layout: Fabrication line and Assembly line.
Fabrication line
  Builds components on a series of machines
  Machine-paced
  Require mechanical or engineering changes to balance

## Slide 42: Repetitive and Product-Oriented Layout
Assembly line
  Puts fabricated parts together at a series of workstations
  Paced by work tasks
  Balanced by moving tasks
Both types of lines must be balanced so that the time to perform the work at each station is the same

## Slide 43: END OF LECTURE